Appendix 1 The inputs for the calculation of the EI  allocation for slab

|  |  | Evirgin 1970 | Evirgin | E virgin m3 | E*virgin (substituted material) | Ereuse | E recycling | E*rec,eol | Edisposal | Qsin/Qp | Qsout/Qp | A | R0 | R1 (LC1) | R2 (LC1) | R1 ( LC2) | R2 ( LC2) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| reinforcing steel | CML2001 - Jan. 2016, Abiotic Depletion (ADP elements) [kg Sb eq.] | 0,0000011 | 0,00000111 | 0,000000857 | 0,00000111 | 0 | 0,000000749 | 0,000000749 | 9,4528E-08 | 1 | 1 | 0,2 |  | 5,00E-01 | 1,00E+00 | 1,00E+00 | 0,95 |
|  | CML2001 - Jan. 2016, Abiotic Depletion (ADP fossil) [MJ] | 28 | 27,7 | 9,83 | 27,7 | 0 | 5,62 | 5,62 | 0,78824 | 1 | 1 | 0,2 |  | 5,00E-01 | 1,00E+00 | 1,00E+00 | 0,95 |
|  | CML2001 - Jan. 2016, Acidification Potential (AP) [kg SO2 eq.] | 0,00681 | 0,00632 | 0,00669 | 0,00632 | 0 | 0,00493 | 0,00493 | 0,00043016 | 1 | 1 | 0,2 |  | 5,00E-01 | 1,00E+00 | 1,00E+00 | 0,95 |
|  | CML2001 - Jan. 2016, Eutrophication Potential (EP) [kg Phosphate eq.] | 0,00394 | 0,00378 | 0,00246 | 0,00378 | 0 | 0,00178 | 0,00178 | 0,000115 | 1 | 1 | 0,2 |  | 5,00E-01 | 1,00E+00 | 1,00E+00 | 0,95 |
|  | CML2001 - Jan. 2016, Freshwater Aquatic Ecotoxicity Pot. (FAETP inf.) [kg DCB eq.] | 0,692 | 0,666 | 1,36 | 0,666 | 0 | 1,15 | 1,15 | 0,1815104 | 1 | 1 | 0,2 |  | 5,00E-01 | 1,00E+00 | 1,00E+00 | 0,95 |
|  | CML2001 - Jan. 2016, Global Warming Potential (GWP 100 years) [kg CO2 eq.] | 1,63 | 1,61 | 0,637 | 1,61 | 0 | 0,374 | 0,374 | 0,05722 | 1 | 1 | 0,2 |  | 5,00E-01 | 1,00E+00 | 1,00E+00 | 0,95 |
|  | CML2001 - Jan. 2016, Global Warming Potential (GWP 100 years), excl biogenic carbon [kg CO2 eq.] | 1,64 | 1,62 | 0,638 | 1,62 | 0 | 0,374 | 0,374 | 0,057068 | 1 | 1 | 0,2 |  | 5,00E-01 | 1,00E+00 | 1,00E+00 | 0,95 |
|  | CML2001 - Jan. 2016, Human Toxicity Potential (HTP inf.) [kg DCB eq.] | 0,579 | 0,566 | 0,968 | 0,566 | 0 | 0,703 | 0,703 | 0,028512 | 1 | 1 | 0,2 |  | 5,00E-01 | 1,00E+00 | 1,00E+00 | 0,95 |
|  | CML2001 - Jan. 2016, Marine Aquatic Ecotoxicity Pot. (MAETP inf.) [kg DCB eq.] | 1700 | 1630 | 1980 | 1630 | 0 | 1620 | 1620 | 62,0608 | 1 | 1 | 0,2 |  | 5,00E-01 | 1,00E+00 | 1,00E+00 | 0,95 |
|  | CML2001 - Jan. 2016, Ozone Layer Depletion Potential (ODP, steady state) [kg R11 eq.] | 3,26E-08 | 3,32E-08 | 5,18E-08 | 3,32E-08 | 0 | 0,00000003 | 0,00000003 | 9,9152E-09 | 1 | 1 | 0,2 |  | 5,00E-01 | 1,00E+00 | 1,00E+00 | 0,95 |
|  | CML2001 - Jan. 2016, Photochem. Ozone Creation Potential (POCP) [kg Ethene eq.] | 0,00131 | 0,00129 | 0,000504 | 0,00129 | 0 | 0,000316 | 0,000316 | 0,000044356 | 1 | 1 | 0,2 |  | 5,00E-01 | 1,00E+00 | 1,00E+00 | 0,95 |
|  | CML2001 - Jan. 2016, Terrestric Ecotoxicity Potential (TETP inf.) [kg DCB eq.] | 0,00501 | 0,00499 | 0,0708 | 0,00499 | 0 | 0,0689 | 0,0689 | 0,000196 | 1 | 1 | 0,2 |  | 5,00E-01 | 1,00E+00 | 1,00E+00 | 0,95 |
| concrete m3 | CML2001 - Jan. 2016, Abiotic Depletion (ADP elements) [kg Sb eq.] | 4,08E-08 | 4,33E-08 | 1,04E-04 | 1,92E-08 | 0 | 0 | 1,92E-08 | 1,84E-08 | 1 | 1,00E+00 | 0,5 |  | 0 | 1 | 1 | 0,9 |
|  | CML2001 - Jan. 2016, Abiotic Depletion (ADP fossil) [MJ] | 5,88E-01 | 5,33E-01 | 1,28E+03 | 5,96E-02 | 0 | 0 | 0,087 | 7,60E-02 | 1 | 1,00E+00 | 0,5 |  | 0 | 1 | 1 | 0,9 |
|  | CML2001 - Jan. 2016, Acidification Potential (AP) [kg SO2 eq.] | 4,46E-04 | 3,36E-04 | 8,06E-01 | 0,0000262 | 0 | 0 | 0,000105 | 3,64E-05 | 1 | 1 | 0,5 |  | 0 | 1 | 1 | 0,9 |
|  | CML2001 - Jan. 2016, Eutrophication Potential (EP) [kg Phosphate eq.] | 1,29E-04 | 9,38E-05 | 2,25E-01 | 0,0000103 | 0 | 0 | 3,35E-05 | 9,81E-06 | 1 | 1 | 0,5 |  | 0 | 1 | 1 | 0,9 |
|  | CML2001 - Jan. 2016, Freshwater Aquatic Ecotoxicity Pot. (FAETP inf.) [kg DCB eq.] | 1,80E-02 | 1,24E-02 | 2,97E+01 | 0,00169 | 0 | 0 | 0,00553 | 8,57E-04 | 1 | 1,00E+00 | 0,5 |  | 0 | 1 | 1 | 0,9 |
|  | CML2001 - Jan. 2016, Global Warming Potential (GWP 100 years) [kg CO2 eq.] | 1,21E-01 | 1,16E-01 | 2,78E+02 | 0,00443 | 0 | 0 | 0,00706 | 4,94E-03 | 1 | 1,00E+00 | 0,5 |  | 0 | 1 | 1 | 0,9 |
|  | CML2001 - Jan. 2016, Global Warming Potential (GWP 100 years), excl biogenic carbon [kg CO2 eq.] | 1,19E-01 | 1,14E-01 | 2,74E+02 | 0,00439 | 0 | 0 | 0,00702 | 4,94E-03 | 1 | 1 | 0,5 |  | 0 | 1 | 1 | 0,9 |
|  | CML2001 - Jan. 2016, Human Toxicity Potential (HTP inf.) [kg DCB eq.] | 2,15E-02 | 1,85E-02 | 4,44E+01 | 0,00399 | 0 | 0 | 0,00611 | 2,29E-03 | 1 | 1 | 0,5 |  | 0 | 1 | 1 | 0,9 |
|  | CML2001 - Jan. 2016, Marine Aquatic Ecotoxicity Pot. (MAETP inf.) [kg DCB eq.] | 4,83E+01 | 3,29E+01 | 7,90E+04 | 4,21E+00 | 0 | 0 | 14,6 | 1,15E+00 | 1 | 1,00E+00 | 0,5 |  | 0 | 1 | 1 | 0,9 |
|  | CML2001 - Jan. 2016, Ozone Layer Depletion Potential (ODP, steady state) [kg R11 eq.] | 3,40E-09 | 3,53E-09 | 8,48E-06 | 4,89E-10 | 0 | 0 | 4,03E-10 | 9,37E-10 | 1 | 1,00E+00 | 0,5 |  | 0 | 1 | 1 | 0,9 |
|  | CML2001 - Jan. 2016, Photochem. Ozone Creation Potential (POCP) [kg Ethene eq.] | 2,68E-05 | 2,23E-05 | 5,35E-02 | 0,00000229 | 0 | 0 | 5,48E-06 | 3,76E-06 | 1 | 1 | 0,5 |  | 0 | 1 | 1 | 0,9 |
|  | CML2001 - Jan. 2016, Terrestric Ecotoxicity Potential (TETP inf.) [kg DCB eq.] | 2,53E-04 | 2,49E-04 | 5,97E-01 | 0,0000813 | 0 | 0 | 7,33E-05 | 1,85E-05 | 1 | 1 | 0,5 |  | 0 | 1 | 1 | 0,9 |
| cement cast floor | CML2001 - Jan. 2016, Abiotic Depletion (ADP elements) [kg Sb eq.] | 1,13E-07 | 1,14E-07 |  | 1,92E-08 | 0 | 0 | 1,92E-08 | 1,81E-08 | 1 | 1,00E+00 | 0,5 |  | 0 | 0,9 | 0 | 0,9 |
|  | CML2001 - Jan. 2016, Abiotic Depletion (ADP fossil) [MJ] | 8,54E-01 | 9,17E-01 |  | 5,96E-02 | 0 | 0 | 0,087 | 7,38E-02 | 1 | 1,00E+00 | 0,5 |  | 0 | 0,9 | 0 | 0,9 |
|  | CML2001 - Jan. 2016, Acidification Potential (AP) [kg SO2 eq.] | 3,46E-04 | 5,26E-04 |  | 0,0000262 | 0 | 0 | 0,000105 | 3,53E-05 | 1 | 1 | 0,5 |  | 0 | 0,9 | 0 | 0,9 |
|  | CML2001 - Jan. 2016, Eutrophication Potential (EP) [kg Phosphate eq.] | 1,01E-04 | 1,54E-04 |  | 0,0000103 | 0 | 0 | 3,35E-05 | 9,49E-06 | 1 | 1 | 0,5 |  | 0 | 0,9 | 0 | 0,9 |
|  | CML2001 - Jan. 2016, Freshwater Aquatic Ecotoxicity Pot. (FAETP inf.) [kg DCB eq.] | 1,19E-02 | 2,07E-02 |  | 0,00169 | 0 | 0 | 0,00553 | 4,83E-04 | 1 | 1,00E+00 | 0,5 |  | 0 | 0,9 | 0 | 0,9 |
|  | CML2001 - Jan. 2016, Global Warming Potential (GWP 100 years) [kg CO2 eq.] | 1,76E-01 | 1,82E-01 |  | 0,00443 | 0 | 0 | 0,00706 | 4,78E-03 | 1 | 1,00E+00 | 0,5 |  | 0 | 0,9 | 0 | 0,9 |
|  | CML2001 - Jan. 2016, Global Warming Potential (GWP 100 years), excl biogenic carbon [kg CO2 eq.] | 1,72E-01 | 1,78E-01 |  | 0,00439 | 0 | 0 | 0,00702 | 4,78E-03 | 1 | 1 | 0,5 |  | 0 | 0,9 | 0 | 0,9 |
|  | CML2001 - Jan. 2016, Human Toxicity Potential (HTP inf.) [kg DCB eq.] | 2,97E-02 | 3,47E-02 |  | 0,00399 | 0 | 0 | 0,00611 | 2,21E-03 | 1 | 1 | 0,5 |  | 0 | 0,9 | 0 | 0,9 |
|  | CML2001 - Jan. 2016, Marine Aquatic Ecotoxicity Pot. (MAETP inf.) [kg DCB eq.] | 3,01E+01 | 5,40E+01 |  | 4,21E+00 | 0 | 0 | 14,6 | 1,02E+00 | 1 | 1,00E+00 | 0,5 |  | 0 | 0,9 | 0 | 0,9 |
|  | CML2001 - Jan. 2016, Ozone Layer Depletion Potential (ODP, steady state) [kg R11 eq.] | 6,50E-09 | 6,34E-09 |  | 4,89E-10 | 0 | 0 | 4,03E-10 | 9,10E-10 | 1 | 1,00E+00 | 0,5 |  | 0 | 0,9 | 0 | 0,9 |
|  | CML2001 - Jan. 2016, Photochem. Ozone Creation Potential (POCP) [kg Ethene eq.] | 3,02E-05 | 3,76E-05 |  | 0,00000229 | 0 | 0 | 5,48E-06 | 3,64E-06 | 1 | 1 | 0,5 |  | 0 | 0,9 | 0 | 0,9 |
|  | CML2001 - Jan. 2016, Terrestric Ecotoxicity Potential (TETP inf.) [kg DCB eq.] | 5,32E-04 | 5,16E-04 |  | 0,0000813 | 0 | 0 | 7,33E-05 | 1,79E-05 | 1 | 1 | 0,5 |  | 0 | 0,9 | 0 | 0,9 |
| sawn timber m3 | CML2001 - Jan. 2016, Abiotic Depletion (ADP elements) [kg Sb eq.] | 1,14E-07 | 1,26E-07 | 7,54E-05 |  | 0 | 0 | 1,89E-07 | 1,15E-07 | 1 | 1,00E+00 | 0,5 |  | 0 | 0,9 | 0 | 0,9 |
|  | CML2001 - Jan. 2016, Abiotic Depletion (ADP fossil) [MJ] | 1,66E+00 | 1,41E+00 | 843 |  | 0 | 0 | 0,189 | 0,251 | 1 | 1,00E+00 | 0,5 |  | 0 | 0,9 | 0 | 0,9 |
|  | CML2001 - Jan. 2016, Acidification Potential (AP) [kg SO2 eq.] | 1,82E-03 | 1,29E-03 | 0,772 |  | 0 | 0 | 6,43E-05 | 8,56E-05 | 1 | 1 | 0,5 |  | 0 | 0,9 | 0 | 0,9 |
|  | CML2001 - Jan. 2016, Eutrophication Potential (EP) [kg Phosphate eq.] | 5,83E-04 | 4,13E-04 | 0,248 |  | 0 | 0 | 3,69E-05 | 9,39E-03 | 1 | 1 | 0,5 |  | 0 | 0,9 | 0 | 0,9 |
|  | CML2001 - Jan. 2016, Freshwater Aquatic Ecotoxicity Pot. (FAETP inf.) [kg DCB eq.] | 8,20E-02 | 5,45E-02 | 32,7 |  | 0 | 0 | 0,00803 | 0,0128 | 1 | 1,00E+00 | 0,5 |  | 0 | 0,9 | 0 | 0,9 |
|  | CML2001 - Jan. 2016, Global Warming Potential (GWP 100 years) [kg CO2 eq.] | -1,24E+00 | -1,26E+00 | -755 |  | 0 | 0 | -1,8 | 0,091 | 1 | 1,00E+00 | 0,5 |  | 0 | 0,9 | 0 | 0,9 |
|  | CML2001 - Jan. 2016, Global Warming Potential (GWP 100 years), excl biogenic carbon [kg CO2 eq.] | 1,27E-01 | 1,04E-01 | 62,2 |  | 0 | 0 | 0,0132 | 0,069 | 1 | 1 | 0,5 |  | 0 | 0,9 | 0 | 0,9 |
|  | CML2001 - Jan. 2016, Human Toxicity Potential (HTP inf.) [kg DCB eq.] | 1,00E-01 | 8,58E-02 | 51,5 |  | 0 | 0 | 0,00958 | 0,0122 | 1 | 1 | 0,5 |  | 0 | 0,9 | 0 | 0,9 |
|  | CML2001 - Jan. 2016, Marine Aquatic Ecotoxicity Pot. (MAETP inf.) [kg DCB eq.] | 2,13E+02 | 1,38E+02 | 8,27E+04 |  | 0 | 0 | 18,4 | 15,7 | 1 | 1,00E+00 | 0,5 |  | 0 | 0,9 | 0 | 0,9 |
|  | CML2001 - Jan. 2016, Ozone Layer Depletion Potential (ODP, steady state) [kg R11 eq.] | 8,90E-09 | 9,55E-09 | 5,73E-06 |  | 0 | 0 | 1,71E-09 | 2,62E-09 | 1 | 1,00E+00 | 0,5 |  | 0 | 0,9 | 0 | 0,9 |
|  | CML2001 - Jan. 2016, Photochem. Ozone Creation Potential (POCP) [kg Ethene eq.] | 2,33E-04 | 2,12E-04 | 0,127 |  | 0 | 0 | 4,75E-06 | 2,12E-05 | 1 | 1 | 0,5 |  | 0 | 0,9 | 0 | 0,9 |
|  | CML2001 - Jan. 2016, Terrestric Ecotoxicity Potential (TETP inf.) [kg DCB eq.] | 1,03E-03 | 1,01E-03 | 0,603 |  | 0 | 0 | 0,0001 | 4,13E-04 | 1 | 1 | 0,5 |  | 0 | 0,9 | 0 | 0,9 |
| insulation (EPS) | CML2001 - Jan. 2016, Abiotic Depletion (ADP elements) [kg Sb eq.] | 4,76E-07 | 5,83E-07 |  |  | 0 | 0 |  | 6,86E-09 | 1 | 1,00E+00 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Abiotic Depletion (ADP fossil) [MJ] | 9,31E+01 | 9,07E+01 |  |  | 0 | 0 |  | 0,0605 | 1 | 1,00E+00 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Acidification Potential (AP) [kg SO2 eq.] | 2,53E-02 | 2,03E-02 |  |  | 0 | 0 |  | 6,43E-05 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Eutrophication Potential (EP) [kg Phosphate eq.] | 5,25E-03 | 3,68E-03 |  |  | 0 | 0 |  | 0,0817 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Freshwater Aquatic Ecotoxicity Pot. (FAETP inf.) [kg DCB eq.] | 7,55E-01 | 5,00E-01 |  |  | 0 | 0 |  | 1,19 | 1 | 1,00E+00 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Global Warming Potential (GWP 100 years) [kg CO2 eq.] | 4,46E+00 | 4,24E+00 |  |  | 0 | 0 |  | 0,144 | 1 | 1,00E+00 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Global Warming Potential (GWP 100 years), excl biogenic carbon [kg CO2 eq.] | 4,43E+00 | 4,22E+00 |  |  | 0 | 0 |  | 0,144 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Human Toxicity Potential (HTP inf.) [kg DCB eq.] | 8,84E-01 | 7,51E-01 |  |  | 0 | 0 |  | 0,394 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Marine Aquatic Ecotoxicity Pot. (MAETP inf.) [kg DCB eq.] | 2,02E+03 | 1,32E+03 |  |  | 0 | 0 |  | 1,09E+03 | 1 | 1,00E+00 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Ozone Layer Depletion Potential (ODP, steady state) [kg R11 eq.] | 1,12E-07 | 1,18E-07 |  |  | 0 | 0 |  | 7,61E-10 | 1 | 1,00E+00 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Photochem. Ozone Creation Potential (POCP) [kg Ethene eq.] | 8,19E-03 | 7,98E-03 |  |  | 0 | 0 |  | 3,13E-05 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Terrestric Ecotoxicity Potential (TETP inf.) [kg DCB eq.] | 1,32E-02 | 1,30E-02 |  |  | 0 | 0 |  | 0,000822 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
| base plaster | CML2001 - Jan. 2016, Abiotic Depletion (ADP elements) [kg Sb eq.] | 4,92E-08 | 5,62E-08 |  |  | 0 | 0 |  | 1,27E-07 | 1 | 1,00E+00 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Abiotic Depletion (ADP fossil) [MJ] | 1,43E+00 | 1,27E+00 |  |  | 0 | 0 |  | 1,87E-01 | 1 | 1,00E+00 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Acidification Potential (AP) [kg SO2 eq.] | 1,14E-03 | 8,08E-04 |  |  | 0 | 0 |  | 4,61E-05 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Eutrophication Potential (EP) [kg Phosphate eq.] | 3,38E-04 | 2,34E-04 |  |  | 0 | 0 |  | 1,37E-05 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Freshwater Aquatic Ecotoxicity Pot. (FAETP inf.) [kg DCB eq.] | 4,94E-02 | 3,25E-02 |  |  | 0 | 0 |  | 0,00129 | 1 | 1,00E+00 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Global Warming Potential (GWP 100 years) [kg CO2 eq.] | 2,48E-01 | 2,34E-01 |  |  | 0 | 0 |  | 0,00764 | 1 | 1,00E+00 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Global Warming Potential (GWP 100 years), excl biogenic carbon [kg CO2 eq.] | 2,43E-01 | 2,29E-01 |  |  | 0 | 0 |  | 0,00763 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Human Toxicity Potential (HTP inf.) [kg DCB eq.] | 4,74E-02 | 3,86E-02 |  |  | 0 | 0 |  | 0,00441 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Marine Aquatic Ecotoxicity Pot. (MAETP inf.) [kg DCB eq.] | 1,34E+02 | 8,78E+01 |  |  | 0 | 0 |  | 2,65E+00 | 1 | 1,00E+00 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Ozone Layer Depletion Potential (ODP, steady state) [kg R11 eq.] | 8,82E-09 | 9,21E-09 |  |  | 0 | 0 |  | 2,29E-09 | 1 | 1,00E+00 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Photochem. Ozone Creation Potential (POCP) [kg Ethene eq.] | 6,68E-05 | 5,32E-05 |  |  | 0 | 0 |  | 4,86E-06 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Terrestric Ecotoxicity Potential (TETP inf.) [kg DCB eq.] | 4,35E-04 | 4,22E-04 |  |  | 0 | 0 |  | 3,67E-05 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
| paint | CML2001 - Jan. 2016, Abiotic Depletion (ADP elements) [kg Sb eq.] | 1,09E-05 | 1,09E-05 |  |  | 0 | 0 |  | 3,80E-08 | 1 | 1,00E+00 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Abiotic Depletion (ADP fossil) [MJ] | 4,66E+01 | 4,58E+01 |  |  | 0 | 0 |  | 0,135 | 1 | 1,00E+00 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Acidification Potential (AP) [kg SO2 eq.] | 2,02E-02 | 1,85E-02 |  |  | 0 | 0 |  | 3,12E-05 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Eutrophication Potential (EP) [kg Phosphate eq.] | 1,08E-02 | 1,03E-02 |  |  | 0 | 0 |  | 9,25E-06 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Freshwater Aquatic Ecotoxicity Pot. (FAETP inf.) [kg DCB eq.] | 1,16E+00 | 1,07E+00 |  |  | 0 | 0 |  | 0,000672 | 1 | 1,00E+00 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Global Warming Potential (GWP 100 years) [kg CO2 eq.] | 2,59E+00 | 2,51E+00 |  |  | 0 | 0 |  | 0,00422 | 1 | 1,00E+00 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Global Warming Potential (GWP 100 years), excl biogenic carbon [kg CO2 eq.] | 2,79E+00 | 2,71E+00 |  |  | 0 | 0 |  | 0,00421 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Human Toxicity Potential (HTP inf.) [kg DCB eq.] | 1,43E+00 | 1,38E+00 |  |  | 0 | 0 |  | 0,00224 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Marine Aquatic Ecotoxicity Pot. (MAETP inf.) [kg DCB eq.] | 2,24E+03 | 1,98E+03 |  |  | 0 | 0 |  | 1,40E+00 | 1 | 1,00E+00 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Ozone Layer Depletion Potential (ODP, steady state) [kg R11 eq.] | 3,52E-07 | 3,54E-07 |  |  | 0 | 0 |  | 1,66E-09 | 1 | 1,00E+00 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Photochem. Ozone Creation Potential (POCP) [kg Ethene eq.] | 1,49E-03 | 1,42E-03 |  |  | 0 | 0 |  | 3,34E-06 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Terrestric Ecotoxicity Potential (TETP inf.) [kg DCB eq.] | 2,64E-02 | 2,63E-02 |  |  | 0 | 0 |  | 2,04E-05 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |

Appendix 2 The inputs for the calculation of the EI allocation  for exterior wall

|  |  | Evirgin 1970 | Evirgin | E virgin m3 | E*virgin (substituted material) | Ereuse | E recycling | E*rec,eol | Edisposal | Qsin/Qp | Qsout/Qp | A | R0 | R1 (1 LC) | R2 (1 LC) | R1 (2 LC) | R2 (2 LC) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| adhesive mortar | CML2001 - Jan. 2016, Abiotic Depletion (ADP elements) [kg Sb eq.] | 5,13E-06 | 5,16E-06 |  |  | 0 |  |  | 1,25E-07 | 1 | 1 | 0,5 |  | 0 | 1 | 1 | 0 |
|  | CML2001 - Jan. 2016, Abiotic Depletion (ADP fossil) [MJ] | 2,04E+01 | 1,96E+01 |  |  | 0 |  |  | 2,47E-01 | 1 | 1 | 0,5 |  | 0 | 1 | 1 | 0 |
|  | CML2001 - Jan. 2016, Acidification Potential (AP) [kg SO2 eq.] | 8,11E-03 | 6,48E-03 |  |  | 0 |  |  | 8,34E-05 | 1 | 1 | 0,5 |  | 0 | 1 | 1 | 0 |
|  | CML2001 - Jan. 2016, Eutrophication Potential (EP) [kg Phosphate eq.] | 3,69E-03 | 3,17E-03 |  |  | 0 |  |  | 2,34E-05 | 1 | 1 | 0,5 |  | 0 | 1 | 1 | 0 |
|  | CML2001 - Jan. 2016, Freshwater Aquatic Ecotoxicity Pot. (FAETP inf.) [kg DCB eq.] | 5,48E-01 | 4,65E-01 |  |  | 0 |  |  | 2,01E-03 | 1 | 1 | 0,5 |  | 0 | 1 | 1 | 0 |
|  | CML2001 - Jan. 2016, Global Warming Potential (GWP 100 years) [kg CO2 eq.] | 1,18E+00 | 1,11E+00 |  |  | 0 |  |  | 1,22E-02 | 1 | 1 | 0,5 |  | 0 | 1 | 1 | 0 |
|  | CML2001 - Jan. 2016, Global Warming Potential (GWP 100 years), excl biogenic carbon [kg CO2 eq.] | 1,17E+00 | 1,10E+00 |  |  | 0 |  |  | 1,22E-02 | 1 | 1 | 0,5 |  | 0 | 1 | 1 | 0 |
|  | CML2001 - Jan. 2016, Human Toxicity Potential (HTP inf.) [kg DCB eq.] | 7,86E-01 | 7,42E-01 |  |  | 0 |  |  | 6,64E-03 | 1 | 1 | 0,5 |  | 0 | 1 | 1 | 0 |
|  | CML2001 - Jan. 2016, Marine Aquatic Ecotoxicity Pot. (MAETP inf.) [kg DCB eq.] | 1,32E+03 | 1,09E+03 |  |  | 0 |  |  | 4,42E+00 | 1 | 1 | 0,5 |  | 0 | 1 | 1 | 0 |
|  | CML2001 - Jan. 2016, Ozone Layer Depletion Potential (ODP, steady state) [kg R11 eq.] | 1,57E-07 | 1,59E-07 |  |  | 0 |  |  | 2,93E-09 | 1 | 1 | 0,5 |  | 0 | 1 | 1 | 0 |
|  | CML2001 - Jan. 2016, Photochem. Ozone Creation Potential (POCP) [kg Ethene eq.] | 6,50E-04 | 5,82E-04 |  |  | 0 |  |  | 8,69E-06 | 1 | 1 | 0,5 |  | 0 | 1 | 1 | 0 |
|  | CML2001 - Jan. 2016, Terrestric Ecotoxicity Potential (TETP inf.) [kg DCB eq.] | 8,46E-03 | 8,39E-03 |  |  | 0 |  |  | 5,76E-05 | 1 | 1 | 0,5 |  | 0 | 1 | 1 | 0 |
| concrete brick | CML2001 - Jan. 2016, Abiotic Depletion (ADP elements) [kg Sb eq.] | 1,72E-07 | 1,74E-07 |  | 1,92E-08 | 0 |  | 5,07E-09 | 1,24E-07 | 1 | 1 | 0,5 |  | 0 | 1 | 1 | 0,9 |
|  | CML2001 - Jan. 2016, Abiotic Depletion (ADP fossil) [MJ] | 7,54E-01 | 6,94E-01 |  | 5,96E-02 | 0 |  | 4,47E-02 | 2,38E-01 | 1 | 1 | 0,5 |  | 0 | 1 | 1 | 0,9 |
|  | CML2001 - Jan. 2016, Acidification Potential (AP) [kg SO2 eq.] | 5,39E-04 | 4,15E-04 |  | 2,62E-05 | 0 |  | 2,46E-05 | 7,80E-05 | 1 | 1 | 0,5 |  | 0 | 1 | 1 | 0,9 |
|  | CML2001 - Jan. 2016, Eutrophication Potential (EP) [kg Phosphate eq.] | 1,71E-04 | 1,32E-04 |  | 1,03E-05 | 0 |  | 6,52E-06 | 2,20E-05 | 1 | 1 | 0,5 |  | 0 | 1 | 1 | 0,9 |
|  | CML2001 - Jan. 2016, Freshwater Aquatic Ecotoxicity Pot. (FAETP inf.) [kg DCB eq.] | 2,79E-02 | 2,16E-02 |  | 1,69E-03 | 0 |  | 2,57E-04 | 1,96E-03 | 1 | 1 | 0,5 |  | 0 | 1 | 1 | 0,9 |
|  | CML2001 - Jan. 2016, Global Warming Potential (GWP 100 years) [kg CO2 eq.] | 1,33E-01 | 1,28E-01 |  | 4,43E-03 | 0 |  | 3,25E-03 | 1,15E-02 | 1 | 1 | 0,5 |  | 0 | 1 | 1 | 0,9 |
|  | CML2001 - Jan. 2016, Global Warming Potential (GWP 100 years), excl biogenic carbon [kg CO2 eq.] | 1,31E-01 | 1,26E-01 |  | 4,39E-03 | 0 |  | 3,25E-03 | 1,15E-02 | 1 | 1 | 0,5 |  | 0 | 1 | 1 | 0,9 |
|  | CML2001 - Jan. 2016, Human Toxicity Potential (HTP inf.) [kg DCB eq.] | 4,74E-02 | 4,41E-02 |  | 3,99E-03 | 0 |  | 1,44E-03 | 6,35E-03 | 1 | 1 | 0,5 |  | 0 | 1 | 1 | 0,9 |
|  | CML2001 - Jan. 2016, Marine Aquatic Ecotoxicity Pot. (MAETP inf.) [kg DCB eq.] | 7,00E+01 | 5,25E+01 |  | 4,21E+00 | 0 |  | 5,29E-01 | 4,31E+00 | 1 | 1 | 0,5 |  | 0 | 1 | 1 | 0,9 |
|  | CML2001 - Jan. 2016, Ozone Layer Depletion Potential (ODP, steady state) [kg R11 eq.] | 4,12E-09 | 4,26E-09 |  | 4,89E-10 | 0 |  | 5,63E-10 | 2,80E-09 | 1 | 1 | 0,5 |  | 0 | 1 | 1 | 0,9 |
|  | CML2001 - Jan. 2016, Photochem. Ozone Creation Potential (POCP) [kg Ethene eq.] | 3,46E-05 | 2,95E-05 |  | 2,29E-06 | 0 |  | 2,53E-06 | 8,14E-06 | 1 | 1 | 0,5 |  | 0 | 1 | 1 | 0,9 |
|  | CML2001 - Jan. 2016, Terrestric Ecotoxicity Potential (TETP inf.) [kg DCB eq.] | 7,89E-04 | 7,84E-04 |  | 8,13E-05 | 0 |  | 1,11E-05 | 5,52E-05 | 1 | 1 | 0,5 |  | 0 | 1 | 1 | 0,9 |
| base plaster | CML2001 - Jan. 2016, Abiotic Depletion (ADP elements) [kg Sb eq.] | 4,92E-08 | 5,62E-08 |  |  | 0 |  |  | 1,27E-07 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Abiotic Depletion (ADP fossil) [MJ] | 1,43E+00 | 1,27E+00 |  |  | 0 |  |  | 1,87E-01 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Acidification Potential (AP) [kg SO2 eq.] | 1,14E-03 | 8,08E-04 |  |  | 0 |  |  | 4,61E-05 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Eutrophication Potential (EP) [kg Phosphate eq.] | 3,38E-04 | 2,34E-04 |  |  | 0 |  |  | 1,37E-05 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Freshwater Aquatic Ecotoxicity Pot. (FAETP inf.) [kg DCB eq.] | 4,94E-02 | 3,25E-02 |  |  | 0 |  |  | 1,29E-03 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Global Warming Potential (GWP 100 years) [kg CO2 eq.] | 2,48E-01 | 2,34E-01 |  |  | 0 |  |  | 7,64E-03 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Global Warming Potential (GWP 100 years), excl biogenic carbon [kg CO2 eq.] | 2,43E-01 | 2,29E-01 |  |  | 0 |  |  | 7,63E-03 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Human Toxicity Potential (HTP inf.) [kg DCB eq.] | 4,74E-02 | 3,86E-02 |  |  | 0 |  |  | 4,41E-03 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Marine Aquatic Ecotoxicity Pot. (MAETP inf.) [kg DCB eq.] | 1,34E+02 | 8,78E+01 |  |  | 0 |  |  | 2,65E+00 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Ozone Layer Depletion Potential (ODP, steady state) [kg R11 eq.] | 8,82E-09 | 9,21E-09 |  |  | 0 |  |  | 2,29E-09 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Photochem. Ozone Creation Potential (POCP) [kg Ethene eq.] | 6,68E-05 | 5,32E-05 |  |  | 0 |  |  | 4,86E-06 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Terrestric Ecotoxicity Potential (TETP inf.) [kg DCB eq.] | 4,35E-04 | 4,22E-04 |  |  | 0 |  |  | 3,67E-05 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
| cover coat | CML2001 - Jan. 2016, Abiotic Depletion (ADP elements) [kg Sb eq.] | 3,13E-05 | 3,13E-05 |  |  | 0 |  |  | 1,28E-07 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Abiotic Depletion (ADP fossil) [MJ] | 1,41E+00 | 1,25E+00 |  |  | 0 |  |  | 1,90E-01 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Acidification Potential (AP) [kg SO2 eq.] | 9,84E-04 | 6,57E-04 |  |  | 0 |  |  | 4,69E-05 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Eutrophication Potential (EP) [kg Phosphate eq.] | 2,89E-04 | 1,86E-04 |  |  | 0 |  |  | 1,15E-04 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Freshwater Aquatic Ecotoxicity Pot. (FAETP inf.) [kg DCB eq.] | 4,54E-02 | 2,86E-02 |  |  | 0 |  |  | 1,29E-02 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Global Warming Potential (GWP 100 years) [kg CO2 eq.] | 1,11E-01 | 9,73E-02 |  |  | 0 |  |  | 7,87E-03 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Global Warming Potential (GWP 100 years), excl biogenic carbon [kg CO2 eq.] | 1,09E-01 | 9,51E-02 |  |  | 0 |  |  | 7,85E-03 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Human Toxicity Potential (HTP inf.) [kg DCB eq.] | 4,17E-02 | 3,29E-02 |  |  | 0 |  |  | 6,37E-03 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Marine Aquatic Ecotoxicity Pot. (MAETP inf.) [kg DCB eq.] | 1,25E+02 | 7,87E+01 |  |  | 0 |  |  | 1,67E+01 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Ozone Layer Depletion Potential (ODP, steady state) [kg R11 eq.] | 1,03E-08 | 1,07E-08 |  |  | 0 |  |  | 2,32E-09 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Photochem. Ozone Creation Potential (POCP) [kg Ethene eq.] | 5,39E-05 | 4,04E-05 |  |  | 0 |  |  | 4,96E-06 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Terrestric Ecotoxicity Potential (TETP inf.) [kg DCB eq.] | 2,98E-04 | 2,84E-04 |  |  | 0 |  |  | 3,97E-05 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
| paint | CML2001 - Jan. 2016, Abiotic Depletion (ADP elements) [kg Sb eq.] | 1,09E-05 | 1,09E-05 |  |  | 0 |  |  | 3,80E-08 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Abiotic Depletion (ADP fossil) [MJ] | 4,66E+01 | 4,58E+01 |  |  | 0 |  |  | 1,35E-01 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Acidification Potential (AP) [kg SO2 eq.] | 2,02E-02 | 1,85E-02 |  |  | 0 |  |  | 3,12E-05 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Eutrophication Potential (EP) [kg Phosphate eq.] | 1,08E-02 | 1,03E-02 |  |  | 0 |  |  | 9,25E-06 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Freshwater Aquatic Ecotoxicity Pot. (FAETP inf.) [kg DCB eq.] | 1,16E+00 | 1,07E+00 |  |  | 0 |  |  | 6,72E-04 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Global Warming Potential (GWP 100 years) [kg CO2 eq.] | 2,59E+00 | 2,51E+00 |  |  | 0 |  |  | 4,22E-03 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Global Warming Potential (GWP 100 years), excl biogenic carbon [kg CO2 eq.] | 2,79E+00 | 2,71E+00 |  |  | 0 |  |  | 4,21E-03 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Human Toxicity Potential (HTP inf.) [kg DCB eq.] | 1,43E+00 | 1,38E+00 |  |  | 0 |  |  | 2,24E-03 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Marine Aquatic Ecotoxicity Pot. (MAETP inf.) [kg DCB eq.] | 2,24E+03 | 1,98E+03 |  |  | 0 |  |  | 1,40E+00 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Ozone Layer Depletion Potential (ODP, steady state) [kg R11 eq.] | 3,52E-07 | 3,54E-07 |  |  | 0 |  |  | 1,66E-09 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Photochem. Ozone Creation Potential (POCP) [kg Ethene eq.] | 1,49E-03 | 1,42E-03 |  |  | 0 |  |  | 3,34E-06 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Terrestric Ecotoxicity Potential (TETP inf.) [kg DCB eq.] | 2,64E-02 | 2,63E-02 |  |  | 0 |  |  | 2,04E-05 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
| rock wool | CML2001 - Jan. 2016, Abiotic Depletion (ADP elements) [kg Sb eq.] | 1,72E-06 | 1,77E-06 |  |  | 0 |  |  | 4,84E-08 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Abiotic Depletion (ADP fossil) [MJ] | 2,01E+01 | 1,92E+01 |  |  | 0 |  |  | 1,46E-01 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Acidification Potential (AP) [kg SO2 eq.] | 1,29E-02 | 1,10E-02 |  |  | 0 |  |  | 3,81E-05 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Eutrophication Potential (EP) [kg Phosphate eq.] | 3,28E-03 | 2,67E-03 |  |  | 0 |  |  | 1,07E-05 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Freshwater Aquatic Ecotoxicity Pot. (FAETP inf.) [kg DCB eq.] | 4,92E-01 | 3,92E-01 |  |  | 0 |  |  | 9,86E-04 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Global Warming Potential (GWP 100 years) [kg CO2 eq.] | 1,25E+00 | 1,17E+00 |  |  | 0 |  |  | 5,16E-03 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Global Warming Potential (GWP 100 years), excl biogenic carbon [kg CO2 eq.] | 1,26E+00 | 1,18E+00 |  |  | 0 |  |  | 5,15E-03 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Human Toxicity Potential (HTP inf.) [kg DCB eq.] | 7,80E-01 | 7,28E-01 |  |  | 0 |  |  | 2,96E-03 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Marine Aquatic Ecotoxicity Pot. (MAETP inf.) [kg DCB eq.] | 1,29E+03 | 1,01E+03 |  |  | 0 |  |  | 2,26E+00 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Ozone Layer Depletion Potential (ODP, steady state) [kg R11 eq.] | 4,55E-08 | 4,78E-08 |  |  | 0 |  |  | 1,72E-09 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Photochem. Ozone Creation Potential (POCP) [kg Ethene eq.] | 7,93E-04 | 7,13E-04 |  |  | 0 |  |  | 4,10E-06 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |
|  | CML2001 - Jan. 2016, Terrestric Ecotoxicity Potential (TETP inf.) [kg DCB eq.] | 4,28E-03 | 4,21E-03 |  |  | 0 |  |  | 2,77E-05 | 1 | 1 | 0,5 |  | 0 | 0 | 0 | 0 |